## Slide 1: Algorithms For Distributed Monitoring In Multi-Channel Ad Hoc Wireless Networks
Donghoon Shin
Ph.D. Final Examination
Advisor: Prof. Saurabh Bagchi
Committee Members: Profs. Ness B. Shroff, Xiaojun Lin, and Chih-Chun Wang
Dependable Computing Systems Lab (DCSL)
School of Electrical and Computer Engineering
Purdue University
Notes:  0.5 min
Good afternoon, everyone. First of all, I would like to thank the committee members and the audience for attending my final examination. The title of this talk is algorithms for distributed monitoring in multi-channel ad hoc wireless networks.

## Slide 2: Outline of the Talk
Introduction and Motivation
Summary of Research until Preliminary Examination
Channel Assignment of Imperfect Sniffers for Reliable Monitoring
Open Issues and Future Directions
Notes: 1 min
First, I will talk about … Next, I will summarize … Then, I will present the last piece of my Ph.D. research, which on …. Lastly, I will discuss the open issues.

## Slide 3: Ad Hoc Wireless Networks (AHWN)
Nodes communicate with each other over a wireless channel
Each node operates not only as a host but also as a router
Easily deployable, decentralized and self-configured
Suitable for a variety of applications that avoid infrastructure
  Establishing infrastructure is impossible
    Examples: battlefield, natural-disaster areas, natural habitat
  Establishing infrastructure is not cost-effective
    Examples: rural areas, temporary events (e.g. sport match, conference)
Internet
Notes:  1 mins
Ad hoc wireless networks consist of a number of nodes communicating with each other over a wireless channel. In these networks, each node operates not only as a host but also as a router forwarding others’ packets. These networks are easily deployable, decentralized, and self-configured.
Such desirable features make ad hoc wireless networks suitable for a variety of applications where no infrastructure is required. For example, they can be deployed in the environments where establishing infrastructure is impossible or not cost-effective.

## Slide 4: Security Vulnerability of AHWN
Adversary can physically capture and tamper with ad hoc nodes
  Ad hoc nodes are often deployed in insecure locations
    Mesh routers are deployed on rooftops or attached to streetlights
    Nodes may be deployed in a hostile environment, e.g., in a battlefield
  Ad hoc nodes are typically low-cost devices that lack strong hardware protection
Compromised nodes can launch a variety of attacks
  DoS (Denial of Service) attacks
    Violation of back-off rule at MAC layer
    (Selectively) dropping packets
  Inject malicious traffic into networks
    DDoS (Distributed DoS) traffic
    Worm traffic
Notes:  1 mins
On the other hand, ad hoc wireless networks are vulnerable to a wide range of security attacks. An adversary can physically capture and tamper with ad hoc nodes. This is because they are often deployed in insecure locations. For example, mesh routers are deployed in open places such as rooftops or streetlights. Some nodes may be deployed even in a hostile environment like battlefield. Also, ad hoc nodes are typically low-cost devices without strong hardware protection. Hence, they are not protected from being tempered
Once nodes are compromised, they can be exploited to launch a variety of attacks. For example, compromised nodes can deny network protocols. Also, they can inject malicious traffic into networks, such as worm traffic.

## Slide 5: Motivation
Use of multiple channels in AHWNs
  Nodes equipped with multiple radios operate on different channels
  Can significantly increase the network capacity
An issue with behavior-based detection in multi-channel AHWNs:
Behavior-based detection to defend AHWNs
  Sniffer nodes overhear communications in their neighborhood, and then determine if the behaviors of the neighbors are legitimate
  Example: to detect the MAC-layer misbehavior, a sniffer can verify if the back-off times of its neighbors follow the legitimate patterns
In order to execute the behavior-based detection, on which channel does a sniffer overhear?
Notes: 1.5 mins
An approach commonly used to defend ad hoc wireless network is behavior-based detection. In this, sniffer nodes overhear communications in their neighborhood exploiting the open nature of wireless medium. Then, they determine if the behaviors of their neighbors are legitimate, based on the observations from the overhearing. For example, to detect MAC-layer misbehavior, a sniffer can verify if the back-off times of its neighbors follow legitimate patterns.
  Recently, it has been extensively studied to use multiple channels in ad hoc wireless networks. In these networks, nodes are equipped with multiple radios operating on different channels. It is known that using multiple channels and multiple radios can significantly increase the capacity of the network.
  A major issue that raises with the behavior-based detection in multi-channel AHWN is optimal placement and channel assignment of sniffers. That is how to …

## Slide 6: Monitoring in Multi-Channel Networks
S2
S3
S1
N7
N1
N3
N2
N5
N4
N6
How to place a set of sniffers and assign a set of channels to the sniffers’ radios so as to capture as large an amount of traffic as possible?
Si: Sniffer
Nj: Node
: On channel 1
: On channel 2
Receiving range of sniffers
Not covered

## Slide 7: Summary of Research until Prelim.
Optimal placement and channel assignment of sniffers [MobiHoc 2009] [Elsevier Ad Hoc Networks (under revision)]
  Showed that the problem is NP-hard, even for 2 channels
  Designed approximation algorithms with a performance guarantee
Distributed channel assignment of sniffers for large-scale networks [INFOCOM 2012, Mini-Conference]
  Studied the optimal channel assignment of sniffers
    Still NP-hard, even for 2 channels
  Developed a distributed algorithm scalable to large networks
Notes: 1 min
In the first part, we studied… We showed that … Then, we developed the best approximation algorithm … For the optimal placement and channel assignment of sniffers,

## Slide 8: Contributions
For OSCA, the best possible approximation ratio (AR) is known as 7/8
  Hence, a gap exists between the lower bound (1-1/e) and the upper bound (7/8)
Problem | Achievements
Optimal placement in single-channel networks (existing work) | GRD-SC, AR: 1-1/e  Best
Optimal placement and channel assignment in multi-channel networks | GRD-MC, AR: 0.5 (even for 2 channels)
 | PRA, AR: 1 – 1/e ≈ 0.632 (probabilistically)
 | DRA, AR: 1 – 1/e (deterministically)  Best
Optimal sniffer-channel assignment (OSCA) | DA-OSCA (distributed algorithm), AR: 1 – 1/e
Notes: 1.5 mins
In this thesis work, we have designed three approximation algorithms for MCMC in a centralized setting. The first is GR-MCMC and it is an intuitive extension of GR-MCSC to MCMC. It achieves only a half approximation ratio. The other two are algorithms based on a technique called LP rounding. The first LP rounding algorithm is PRA, and it achieves an approximation ratio of 1-1/e probabilistically, which is the best approximation ratio for MCMC. The second LP rounding algorithm is DRA, and it achieves the best approximation ratio deterministically.
Also, we have designed three distributed approximation algorithms based on the centralized algorithms. They are DGR-MCMC, DPRA, and DDRA. All of these three distributed algorithms have the same approximation ratios as their centralized counterparts.

## Slide 9: Road Map
Introduction and Motivation
Summary of Research until Preliminary Examination
Channel Assignment of Imperfect Sniffers for Reliable Monitoring
Open Issues and Future Directions
Notes: 5 mins up to here
Now, I will present the third part of my Ph.D. research, which is on …

## Slide 10: Outline
Motivation and Contributions
Problem Formulation
Proposed Approximation Algorithms
Simulation Results
Conclusion
Notes: 1 min
  This is the outline. First I will talk about motivation and our contributions. Next, I will describe the problem formulation. Then, I will present our proposed approximation algorithms, and then we will see simulation results of the proposed algorithms. Lastly, I will discuss the conclusion.

## Slide 11: Motivation
Our prior works assumed that sniffers are perfect
In practice, sniffers may probabilistically stop functioning and/or generate erroneous reports on monitoring due to:
  Poor reception (due to packet collisions or poor channel conditions)
  Compromise by an adversary
  Operational failure
  Sleep mode for energy saving
However, we would like to still maintain the accuracy of monitoring above a certain level
Solution approach: Provide sniffer redundancy to each node
  That is, each node has to meet a coverage requirement, i.e., the minimum number of sniffers required to reliably monitor the node
Notes: 1.5 mins
  In our previous works, we assumed that … This implies that once a node has a sniffer within its transmission range operating on the same channel, the node’s activity will be always monitored without any error

## Slide 12: Contributions
Study the maximum coverage problem with multi-cover requirements
  Viewed as a generalization from the maximum coverage problem with single-cover requirement (i.e., for the perfect sniffers)
Show that the generalized maximum coverage problem becomes more difficult than the special case
  Submodular property does not hold in the general cases
  Performance guarantees of the prior algorithms no longer apply
Propose a variety of approximation algorithms
Present an empirical performance analysis of the proposed algorithms through simulations in practical networks
Notes: 1 min
In this work, we study

## Slide 13: Road Map
Motivation and Contributions
Problem Formulation
Proposed Approximation Algorithms
Simulation Results
Conclusion
Notes: 9 mins up to here

## Slide 14: Notation & Terminology
N: Set of nodes
  Assume that each node’s radio is tuned to a specific wireless channel
wn: Weight assigned to node n
  Captures various application-specific objectives of monitoring
rn: Coverage requirement assigned to node n
  Minimum number of sniffers required to reliably monitor node n
S: Set of sniffers
C: Set of available wireless channels
Ks,c: Coverage-set of sniffer s on channel c
  Contains the nodes that can be overheard by sniffer s operating on channel c
Sniffer-channel assignment: A collection of coverage-sets that include only one coverage-set for each sniffer
Notes: Now, I will define the notation and terminology.
we mathematically formulate the optimization problem. First of all, we define notations. In this talk, for ease of exposition, we consider only single-radio networks. However, for the general multi-radio networks, one can extend the results provided here. Please refer to the document.
  There are $n$ normal nodes in the network, $u_1$ through $u_n$. Each normal node’s radio is tuned to a specific wireless channel among $c$ possible channels. We are given $m$ monitoring nodes, $v_1$ through $v_m$. We define coverage-set $S_{ij}$ as the set of the normal nodes that can be overheard if $vi$ tunes its radio to channel $j$. We define group $S_i$ as the collection of the coverage-sets of $v_i$. We denote the collection of all coverage sets by $S$. The maximum number of monitoring nodes that can be chosen is $k$.

## Slide 15: MCRM and NP-hardness
Maximum-Coverage Reliable Monitoring (MCRM):
  A node is covered if it is overhead by at least rn sniffers
To find a sniffer-channel assignment that maximizes the total weight of nodes being covered
For any ε > 0, it is NP-hard to solve MCRM within a factor of 7/8 + ε of the maximum coverage, even for |C| = 2 and rn = 2 for all n
Corollary 1
  Complexity grows exponentially with the number of sniffers
MCRM is NP-hard, even for |C| = 2 and rn = 2 for all n
Corollary 2:
Notes: 1 min
Alternatively, we turn our attention to an optimization problem corresponding to FCRM, which we call the Maximum … MCRM is to find … Since we can find the answer to the FCRM by solving its corresponding optimization problem MCRM, it is also NP-hard to solve MCRM. Further, we have shown the following corollary on inapproximability of MCRM. Thus, for MCRC, no polynomial time algorithm can achieve an approximation ratio higher than 7/8, unless P = NP.
MCRM can be viewed as a generalization from the optimal sniffer-channel assignment without requiring sniffer redundancy. However, the generalized MCRM is essentially different from the special case. To show this, I will first introduce a notion called submodularity, which is an important property in discrete optimization.

## Slide 16: Submodularity
Definition: A real-valued function f : 2S  R, defined on subsets of a finite set S, is said to be submodular if and only if
Intuitively, submodularity is a diminishing-return property
Submodularity allows to efficiently find provably (near-)optimal solutions
  Similar to convexity in continuous optimization
Known that non-submodular functions are difficult to deal with
  In the literature of theoretical computer science, there are little results on provable performance guarantees for non-submodular functions
Notes:  1.5 mins
This is the definition. A real-valued function … Intuitively, this condition says that the return is diminishing as we add an element to a larger set.

## Slide 17: Submodularity of MCRM-SC
w(A): Weight function to compute the total weight of the nodes covered by the sniffer-channel assignment A
Theorem 2:
For MCRM-SC, the weight function w is submodular
1
0
1
2
3
# of sniffers overhearing node n
Coverage of node n with rn = 1
Non-increasing as the given A becomes a superset
MCRM-SC: A special case of MCRM where every node requires a single cover of sniffer
  That is, rn = 1 for all n
Notes: 1.5 mins
We first consider the special case.
To see this, observe that the coverage of node n has an increment only when the number of sniffers overhearing the node n increases from 0 to 1. Hence, the increment of the total weight is non-increasing, as the given sniffer-channel assignment A becomes a superset. Thus, the submodularity holds for MCRM-SC.

## Slide 18: Non-submodularity of MCRM-MC
MCRM-MC: General cases of MCRM where at least one node requires multiple covers of sniffers
  That is, rn ≥ 2 for some n
Theorem 3:
For MCRM-MC, the weight function w is not submodular
For example, suppose K1,1 = {n1, n2}, K2,1 = {n1}, and rn = 2 and wn = 1 for all n
Notes: 1.5 mins
Next, we consider the general cases. By MCRM-MC, we refer to general cases…
We can see this with this simple coun.

## Slide 19: Road Map
Motivation and Contributions
Problem Formulation
Proposed Approximation Algorithms
Simulation Results
Conclusion
Notes: 17 mins up to here

## Slide 20: Naïve Greedy Algorithms for MCRM-MC
At each iteration, pick a coverage-set that is best in terms of:
  Variant 1: the coverage improvement
  Variant 2: the total weight of the uncovered nodes
Illustrative example: wn = 1 and rn = 2 for all n,
  Sniffer 1: K1,1 = {n1, n2, n3, n4}, K1,2 = {n5, n6, n7}
  Sniffer 2: K2,1 = {n1}, K2,2 = {n5, n6, n7}
  Sniffer 3: K3,1 = {n2}, K3,2 = {n8, n9, n10}
  Sniffer 4: K4,1 = {n11, n12, n13}, K4,2 = {n8, n9}
  Variant 1’s selection: {K1,1, K2,1, K3,1, K4,1}  Coverage: {n1, n2}
Optimal selection: {K1,2, K2,2, K3,2, K4,2}  Coverage: {n5, …, n9}
   Myopic decisions of the naïve greedy algorithms leads to poor coverage
  Variant 2’s selection: {K1,1, K2,2, K3,2, K4,1}  Coverage: None
Notes:  2 mins
  First, we consider naive greedy algorithms. Poor performance due to the lack of verification of whether the uncovered nodes can be indeed covered at later steps
  SB: Change the wording of variant 2 to clarify “uncovered nodes”.

## Slide 21: Look-Ahead Greedy Algorithms
At each iteration, consider combinations of multiple coverage-sets to find the best coverage-set(s)
Two variants:
  Variant 1: Look-t-steps-ahead greedy algorithm
    At each step, picks one coverage-set through the procedure:
    Find a collection of t + 1 coverage-sets that achieve the maximum coverage improvement for the current step and the next t steps
    Among the coverage-sets in the selected collection, picks one coverage-set that maximizes coverage improvement at the current step
  Variant 2: t-sniffers-at-one-step greedy algorithm
    At each step, picks a collection of at most t coverage-sets that maximize the per-sniffer coverage improvement
Notes:  1.5 mins
  Inspired by the observation through the example, we design look-ahead greedy algorithms.

## Slide 22: Look-Ahead Greedy Algorithms
Illustrative example: wn = 1 and rn = 2 for all n
  Sniffer 1: K1,1 = {n1, n2, n3, n4}, K1,2 = {n5, n6, n7}
  Sniffer 2: K2,1 = {n1}, K2,2 = {n5, n6, n7}
  Sniffer 3: K3,1 = {n2}, K3,2 = {n8, n9, n10}
  Sniffer 4: K4,1 = {n11, n12, n13}, K4,2 = {n8, n9}
  Look-1-step-ahead greedy algorithm’s selection: {K1,2, K2,2, K3,2, K4,2}  Coverage: {n5, …, n9}
Optimal selection: {K1,2, K2,2, K3,2, K4,2}  Coverage: {n5, …, n9}
   At each step, looking one step further or considering another sniffer jointly enables to make good decisions
  2-sniffers-at-one-step greedy algorithm’s selection: {K1,2, K2,2, K3,2, K4,2}  Coverage: {n5, …, n9}
Look-1-step-ahead greedy algorithm
2-sniffers-at-one-step greedy algorithm
Notes:  1.5 mins, totally 22 mins up to here
  Poor performance due to the greediness to maximize the improvement at the current step
  Poor performance due to the lack of verification of whether the uncovered nodes can be indeed covered at later steps
  SB: If there are N coverage sets total and we did N-step lookahead (variant 1) or N-sniffer-at-once (variant 2), that would be the optimal solution.

## Slide 23: Overview of Relaxation and Rounding
Formulate the given optimization problem into:
  Integer Linear Program (ILP)
  Quadratically Constrained Linear Program (QCLP)
Transform the ILP/QCLP into a relaxed program
  ILP  Linear Program (LP)
  QCLP  SemiDefinite Program (SDP)
Solve the relaxed program to find the optimal solution
  Employing one of existing LP/SDP solvers
Round the non-integer values of the optimal solution to an integer solution that is feasible for the original ILP/QCLP
  Randomized Rounding Algorithm (RRA)
  Greedy Rounding Algorithm (GRA)
Notes: 1.5 mins
At Step 2, an important issue is to find as strong a relaxed program as possible while keeping the relaxed program solvable in polynomial time. The benefit of a stronger relaxed program (i.e., that has a smaller set of constraints including the optimal IP solution) lie in two folds. First, it often leads to a better approximate solution to the IP, since a stronger relaxed program will likely yield a non-integer solution closer to the optimal IP solution. Second, it will possibly provide a better estimate (i.e., upper bound) of the maximum achievable coverage.
At Step 4, a challenging goal is to minimize the degradation of the quality of the resulting integer solution so as to obtain an integer solution that is as close to the optimal IP solution as possible.

## Slide 24
Last constraint makes xn = 0 if the number of sniffers that can overhear node n is smaller than the coverage requirement rn
ILP:
Relaxed
Make LP tighter
ys, c = 1 ↔ Ks, c is chosen
xn = 1 ↔ node n is covered
LP Relaxation
Naïve LP relaxation
Notes:  1 min

## Slide 25: SDP Relaxation
Quadratically Constrained Linear Program (QCLP):
Added
Will result in a tighter SDP relaxation
Makes xn = 1 if node n is covered by the solution; otherwise, xn = 0
Notes:  1 min

## Slide 26: SDP Relaxation
Relaxed to
Define
Transform QCLP with the additional constraints into the equivalent matrix form:
Theorem 4:
The SDP relaxation is at least as strong as the LP relaxation
Zi,j represents a quadratic term zi zj
Positive semidefinite
Matrix of new variables Zi,j
Notes:  1 min

## Slide 27: Rounding Algorithms
Randomized Rounding Algorithm (RRA)
  Probabilistically round the optimal LP/SDP solution {ys,c*} such that:
    where Ys,c is the resulting integer value after rounding
P(Ys,c = 1) = ys,c*
Greedy Rounding Algorithm (GRA)
  Round the optimal LP/SDP solution {ys,c*} by choosing one by one the sniffer-channel pairs whose fractional value will be rounded to 0
  At each iteration,
    For each sniffer-channel pair (s, c) whose value is not rounded to an integer, adjust the fractional values of the sniffer s according to:
    Find the sniffer-channel pair (s#, c#) whose associated adjusted values achieve the maximum coverage improvement
    Update the fractional values of sniffer s# to the adjusted values
Notes: 2 mins

## Slide 28: Time Complexity Analysis
|S|: Number of sniffers
|C|: Number of channels
|N|: Number of nodes
t: Number of steps that the algorithm looks ahead
|N|+|S||C|: Number of variables (i.e., xn’s, ys,c’s ) in ILP/QCLP
Algorithm | Time Complexity
Look-t-Steps-Ahead Greedy | O(¦S¦t+2¦C¦t+1¦N¦)
t-Sniffer-at-One-Step Greedy | O(¦S¦t+2¦C¦t+1¦N¦)
LP-relaxation + RRA/GRA | O( (¦N¦ + ¦S¦¦C¦)3 / log(¦N¦ + ¦S¦¦C¦) )
SDP-relaxation + RRA/GRA | O( (¦N¦ + ¦S¦¦C¦)3 )
RRA | O(¦S¦¦C¦)
GRA | O(¦S¦2¦C¦2¦N¦)
Notes: Now I will present the time complexities of the proposed algorithms. We have the four input parameters, ...
Thus, the time complexities of the LP-relaxation and rounding and the SDP-relaxation and rounding are the time

## Slide 29: Road Map
Motivation and Contributions
Problem Formulation
Proposed Approximation Algorithms
Simulation Results
Conclusion
Notes: 1 min
  Now, we see simulation results of the proposed algorithms

## Slide 30: Simulation Settings
Two metrics
  Coverage
  Running time
Two kinds of networks
  Random network: Nodes are randomly deployed in the network with a uniform distribution
  Scale-free network: Nodes are deployed such that the distribution of the nodes with degree d follows a power law in a form of d-r
Parameter settings
  |N| = 40
  |C| = 3
  wn = 1, rn = 2 for all nodes

## Slide 31: Coverage in Random Network
Look-ahead greedy algorithms show reasonably good performance (at least 92% of maximum coverage), superior to the naïve greedy algorithms
SDP + GRA and LP + GRA show coverage comparable to the maximum achievable coverage (i.e., at least 95% and 94% of maximum coverage)
After rounding, GRA maintains the solution quality closer to the maximum coverage, while RRA results in the degradation of the solution quality
Look-ahead greedy algorithms
Naïve greedy algorithms

## Slide 32: Coverage in Scale-free Network
SDP-based algorithms show a higher coverage improvement (by 2~5%), compared to LP-based algorithms, than in random network
  SDP relaxation shows a noticeable improvement on the upper bound of the maximum achievable coverage (by 4~7%)
SDP-based algorithms
LP-based algorithms

## Slide 33: Running Time in Random Network
LP-based algorithms show the fastest running times
CPU: 2.4 GHz
Memory: 4 GB
Bus: 1.07 GHz
y-axis for look-ahead greedy algorithms (10x left y-axis)
y-axis for the other algorithms
LP-based algorithms
SDP-based algorithms show reasonably fast running times
Look-ahead greedy algorithms show the slowest running times
  Grow rapidly as the number of sniffers increases
  Running time of the t-sniffers-at-one-step greedy algorithm is almost half of the running time of the look-t-steps-ahead greedy algorithm
SDP-based algorithms
Look-ahead algorithms
Notes: 3 mins (5 mins in total)
This implies that,
at each iteration of the while loop, the t-sniffers-at-one-step
greedy algorithm performed channel assignment mostly for
two sniffers, while the look-t-steps-ahead greedy algorithm
did for only one sniffer. But, the t-sniffers-at-one-step greedy
algorithm still shows the coverage comparable to that of the
look-t-steps-ahead greedy algorithm.

## Slide 34: Conclusion
SDP + GRA achieves the highest coverage close to the maximum achievable coverage, but shows a (relatively) long running time
  Favored, especially, for monitoring applications where a higher coverage is more emphasized (e.g., critical security monitoring)
LP + GRA attains the coverage comparable to the coverage of the SDP + GRA, and also shows a fast running time
  A good compromise between coverage and running-time
  Favored for monitoring applications requiring fast running-time (e.g., monitoring dynamic network environments)
Notes: 3 mins (5 mins in total)

## Slide 35: Road Map
Introduction and Motivation
Summary of Research until Preliminary Examination
Channel Assignment of Imperfect Sniffers for Reliable Monitoring
Open Issues and Future Directions
Notes: 5 mins up to here
Now, I will present the third part of my Ph.D. research, which is on …

## Slide 36: Open Issues and Future Directions
Fundamental open issues
  Closing a gap between the lower bound (1-1/e) and the upper bound (7/8) for the optimal sniffer channel assignment
  Achieving provable performance guarantees on the maximum coverage problem with multi-cover requirements
    Analysis on the performance guarantees of our proposed algorithms
    Design and analysis of new approximation algorithms with provable performance guarantees
Future direction
  On how to learn the prior information of the network topology and the channel usage of nodes
    Incorporate the exploration of unknown information
    Analysis of the tradeoff between exploration of unknown information and exploitation of the current knowledge

## Slide 37: Summary
Studied the optimal placement and channel assignment of sniffers in multi-channel ad hoc wireless networks
Mathematically formulated the optimization problem, and showed that the problem is NP-hard
Designed approximation algorithms with a provable performance guarantee
Developed a distributed algorithm scalable to large networks
Allowed for imperfect sniffers, and proposed a solution approach to provide sniffer redundancy and various approximation algorithms
Optimal placement and channel assignment in multi-channel networks | GRD-MC, AR: 0.5 (even for 2 channels)
 | PRA, AR: 1 – 1/e ≈ 0.632 (probabilistically)
 | DRA, AR: 1 – 1/e (deterministically)  Best
Optimal sniffer-channel assignment (OSCA) | DA-OSCA (distributed algorithm), AR: 1 – 1/e

## Slide 38: Thank You
Questions?
Notes: This is the end of my presentation and thank you.

## Slide 39: Monitoring in Single-Channel Network
[JSAC’06, INFOCOM’06] studied the optimal placement of sniffers in single-channel wireless networks, with two objectives:
  Maximizing detection coverage subject to bounded resource consumption
  Minimizing resource consumption while maintaining a desired detection rate
Both are NP-hard problems
Developed greedy approximation algorithms
  Achieve the best possible approximation ratio (unless P = NP)
    For the coverage maximization, 1 – 1/e
    For the resource minimization, O(ln N) where N is the number of sniffers
D. Subhadrabandhu, S. Sarkar, and F. Anjum, “A Framework for Misuse Detection in Ad Hoc Networks—Part I, II,” IEEE JSAC, 2006
D. Subhadrabandhu, S. Sarkar, and F. Anjum, “A Statistical Framework for Intrusion Detection in Ad Hoc Networks,” IEEE INFOCOM, 2006
Notes: 1.5 mins
An approach commonly used to defend ad hoc wireless network is behavior-based detection. In this, nodes overhear communications in their neighborhood exploiting the open nature of wireless medium. Then, they determine if the behaviors of their neighbors are legitimate, based on the observations from the overhearing. For example, to detect MAC-layer misbehavior, a node can verify if the back-off times of its neighbors follow legitimate patterns.
  Recently, it has been extensively studied to use multiple channels and multiple radios in ad hoc wireless networks, especially in wireless mesh networks. In these networks, nodes are equipped with multiple radios that are tuned on different non-overlapping channels. It has been shown that using multiple channels and multiple radios can significantly increase the capacity of ad hoc wireless networks.
  However, the use of multiple channels poses a question to the nodes executing the behavior-based detection. “On which channel to overhear?”

## Slide 40: Related Work – in Multi-Channel Net.
[MobiHoc’10] studied the optimal sniffer-channel assignment to achieve the maximum coverage
  Considered two different capabilities of sniffers’ capturing traffic
    User-centric model
      Assumes that frame-level information can be captured
      Activities of different users are distinguishable.
    Sniffer-centric model
      Assumes that only binary information is available regarding channel activities,
      That is, whether some user is active in a specific channel near a sniffer.
  Devised a stochastic inference scheme that transforms the sniffer-centric model into the user-centric domain
A. Chhetri, H. Nguyen, G. Scalosub, and R. Zheng, “On Quality of Monitoring for Multi-channel Wireless Infrastructure Networks,” ACM MobiHoc, 2010
Notes: 1.5 mins
their focus or performance guarantee is different from
that of this dissertation.

## Slide 41
Running Time for Scale-free Network
Notes: 3 mins (5 mins in total)

## Slide 42: Randomized Rounding Algorithm
Probabilistically round the optimal LP/SDP solution {ys,c*} such that:
  where Ys,c is a binary random variable to denote the resulting integer value after rounding
P(Ys,c = 1) = ys,c*
Procedure: For each sniffer s, select the channel for which a head is first shown through the repeated coin tosses:
  For each channel c, toss a biased coin with the probability of head being:
    where I is the set of channel indices for which a tail was shown
Notes: 3 mins (5 mins in total)

## Slide 43: FCRM and NP-hardness
Full-Coverage Reliable Monitoring (FCRM):
  A node is covered if it is overhead by at least rn sniffers
To determine whether there exists a sniffer-channel assignment that achieves the full coverage
Theorem 1:
  FCRM(k, {rn}) denotes FCRM with k number of channels and the set of coverage requirements {rn}
  Complexity grows exponentially with the number of sniffers
For fixed k ≥ 2 and {rn}, it is NP-hard to solve FCRM(k, {rn})
Notes: 1 min
We are interested in a decision problem called the full-coverage reliable monitoring, which is to determine whether …